## Slide 1: Computer Vision
Part 2: Edge Detection
ADF – Start 09:40

## Slide 2: Agenda
Part 1: Filtering and Convolution
Part 2: Edge Detection
  Edge and Derivative
  Prewitt, Sobel, Marr-Hildreth, and Canny Edge Detector
Computer Vision

## Slide 3: Edges
Computer Vision

## Slide 4: Edges
Discontinuities in images
Edges occur where the contrast changes in the scene,
and hence represent shape and structure information contained in the scene.
Computer Vision

## Slide 5: Edges
Features that are often useful for initializing an image analysis procedure.
Important information for understanding an image
By moving “non-edge” data we also simplify the data.
Computer Vision

## Slide 6: Edge Models
An edge is a place of rapid change in the image intensity function
Computer Vision

## Slide 7: Image Histogram
Computer Vision

## Slide 8: Origins of Edges
Computer Vision
Depth discontinuity
Surface normal discontinuity
Surface color discontinuity
Illumination discontinuity

## Slide 9: Edge Detection Technique
Computer Vision

## Slide 10: Edges Detection
Identify sudden changes (discontinuity) in an image
  Most semantic and shape information can be encoded in edges
  Marks the border of an object
  More compact than pixels
Computer Vision

## Slide 11: Edge Detection Evaluation
Computer Vision
Precision
Recall
Ground Truth
Results of Model
False Positives (FP)
True Positives (TP)
False Negative (FN)
True Negative (TN)

## Slide 12: Edge Detection Evaluation
Good detection:
  find all real edges,
  ignoring noise or other artifacts
Good localization:
  as close as possible to the true edges
  one point only for each true edge point
Computer Vision

## Slide 13: Edge Detection Evaluation
Computer Vision

## Slide 14: 45 Years History of Edge Detection
Computer Vision
[Pre-Deep Learning]

## Slide 15: Edge Models
An edge is a place of rapid change in the image intensity function
Computer Vision
image
intensity function
(along horizontal scanline)
first derivative
edges correspond to
extrema of derivative

## Slide 16: Derivative
Computer Vision

## Slide 17: Derivatives
Derivative: Rate of change
  Speed is a rate of change of a distance,
  Acceleration is a rate of change of speed,
Computer Vision

## Slide 18: Discrete Derivatives / Finite Difference
Images are discrete
Computer Vision
Backward difference
Forward difference
Central difference

## Slide 19: Finite Difference: 1D Example
Derivative masks
  Backward difference
  Forward difference
  Central difference
Computer Vision
 | 10 | 15 | 10 | 10 | 25 | 20 | 20 | 20
 | 10 | 15 | 10 | 10 | 25 | 20 | 20 | 20
 | 0 | -10+15 | -15+10 | -10+10 | -10+25 | -25+20 | -20+20 | -20+20
 | 0 | 5 | -5 | 0 | 15 | -5 | 0 | 0
 | 0 | -10+15 | -15+10 | -10+10 | -10+25 | -25+20 | -20+20 | -20+20
 | 0 | 5 | -5 | 0 | 15 | -5 | 0 | 0
 | 0 | -0+5 | -5+(-5) | -(-5)+0 | -0+15 | -15+(-5) | -(-5)+0 | -0+0
 | 0 | 5 | -10 | 5 | 15 | -20 | 5 | 0
 | 0 | -0+5 | -5+(-5) | -(-5)+0 | -0+15 | -15+(-5) | -(-5)+0 | -0+0
 | 0 | 5 | -10 | 5 | 15 | -20 | 5 | 0

## Slide 20: Derivative in 2D
Given function
Gradient vector
Computer Vision

## Slide 21: Derivative in 2D
Given function
Gradient vector
Gradient magnitude
Gradient direction
Computer Vision

## Slide 22: Derivative of Images Example
Computer Vision
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
-1 | 0 | 1

## Slide 23: Derivative of Images Example
Computer Vision
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
1
0
-1

## Slide 24: Derivative of Images
Computer Vision
Derivative masks

## Slide 25: Derivative of Images Example
Computer Vision
0 | 0 | 0 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 10 | 10 | 0 | 0
0 | 0 | 0 | 0 | 0
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20

## Slide 26: Derivative of Images Example
Computer Vision
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20
10 | 10 | 20 | 20 | 20

## Slide 27: Edges in Image
Computer Vision

## Slide 28: Edges in Image
Computer Vision
Original Image
x-direction
Gradient magnitude
y-direction

## Slide 29: Image Noise
Computer Vision

## Slide 30: Image Noise
Computer Vision

## Slide 31: Intensity profile
Computer Vision

## Slide 32: Image Histogram
Computer Vision

## Slide 33: Effects of Noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Computer Vision

## Slide 34: Effects of Noise
If the signal has noises, The derivative won’t be clear
Computer Vision

## Slide 35: Effects of Noise
Computer Vision
Sensitive to “tiny” edges

## Slide 36: Effects of Noise
Difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What can we do about it?
Computer Vision

## Slide 37: Solution: Smoothing
Computer Vision

## Slide 38: Solution: Smoothing
Convolution is differentiable
Saves us one operation
Computer Vision

## Slide 39: Smoothing Problem
Smoothing removes noise, but blurs edge.
Computer Vision
Smoothed (3x3)
Smoothed (1x1)
Smoothed (7x7)

## Slide 40: Unsharp Masking
Lower Noise, Higher Contrast
Not only noise removal, but edge enhancement is necessary
  Edges are located in high frequency of the images
Computer Vision

## Slide 41: Prewitt and Sobel Edge Detector
Computer Vision

## Slide 42: Prewitt and Sobel Edge Detector
Compute derivatives in and directions
Find gradient magnitude
Threshold gradient magnitude
Computer Vision
threshold

## Slide 43: Prewitt and Sobel Edge Detection
Original image
Laplacian operator
Horizontal derivative
Vertical derivative
Computer Vision

## Slide 44: Prewitt Edge Detector [1970]
Computer Vision
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
1
1
1
blurred
edges in x
average
smoothing in x
1 | 0 | -1
derivative filtering in x
image
1 | 1 | 1
blurred
edges in y
average
smoothing in y
1
0
-1
derivative filtering in y
1 | 1 | 1
0 | 0 | 0
-1 | -1 | -1

## Slide 45: Prewitt Edge Detector [1970]
Computer Vision
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
1 | 1
1 | 1
1 | 1
blurred
edges in x
average
smoothing in x
1 | -1
derivative filtering in x
image
1 | 1 | 1
1 | 1 | 1
blurred
edges in y
average
smoothing in y
1
-1
derivative filtering in y
1 | 1 | 1
0 | 0 | 0
-1 | -1 | -1

## Slide 46: Vertical Edge Detection
Computer Vision
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
0 | 60 | 60 | 0
0 | 60 | 60 | 0
0 | 60 | 60 | 0
0 | 60 | 60 | 0

## Slide 47: Vertical Edge Detection
Computer Vision
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
0 | -60 | -60 | 0
0 | -60 | -60 | 0
0 | -60 | -60 | 0
0 | -60 | -60 | 0

## Slide 48: Horizontal Edge Detection
Computer Vision
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
20 | 20 | 20 | 0 | 0 | 0
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
0 | 0 | 0 | 20 | 20 | 20
1 | 1 | 1
0 | 0 | 0
-1 | -1 | -1
0 | 0 | 0 | 0
60 | 20 | -20 | -60
60 | 20 | -20 | -60
0 | 0 | 0 | 0
Notes: tends to average things a little too much: when applied to one specific row, we lose much of what makes the detail of this specific row

## Slide 49: Sobel Edge Detector [1968]
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1
2
1
blurred
edges in x
average
smoothing in x
1 | 0 | -1
derivative filtering in x
image
1 | 2 | 1
blurred
edges in y
average
smoothing in y
1
0
-1
derivative filtering in y
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
Notes: get an improved estimate of the gradient by averaging the horizontal, vertical and diagonal central differences. Now when you break the gradient into vertical and horizontal components, the diagonal central differences are included in both, while the vertical and horizontal central differences are only included in one. Two avoid double counting the diagonals should therefore have half the weights of the vertical and horizontal.

## Slide 50: Sobel Edge Detector [1968]
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 1
2 | 2
1 | 1
blurred
edges in x
average
smoothing in x
1 | -1
derivative filtering in x
image
1 | 2 | 1
1 | 2 | 1
blurred
edges in y
average
smoothing in y
1
-1
derivative filtering in y
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
Notes: get an improved estimate of the gradient by averaging the horizontal, vertical and diagonal central differences. Now when you break the gradient into vertical and horizontal components, the diagonal central differences are included in both, while the vertical and horizontal central differences are only included in one. Two avoid double counting the diagonals should therefore have half the weights of the vertical and horizontal.

## Slide 51: Sobel Edge Detector
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
Vertical Edge
(absolute value)
Horizontal Edge
(absolute value)

## Slide 52: Sobel Edge Detector
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
threshold
image
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
edges

## Slide 53: Sobel Edge Detector
threshold
edges
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1

## Slide 54: Sobel Edge Detector
Computer Vision
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1

## Slide 55: Basic Comparisons of Edge Operators
Computer Vision
-1 | -2 | 0 | 2 | 1
-2 | -3 | 0 | 3 | 2
-3 | -5 | 0 | 5 | 3
-2 | -3 | 0 | 3 | 2
-1 | -2 | 0 | 2 | 1
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
0 | 1
-1 | 0
Gradient:
Roberts (2x2)
Sobel (3x3)
Sobel (5x5)
1 | 2 | 3 | 2 | 1
2 | 3 | 5 | 3 | 2
0 | 0 | 0 | 0 | 0
-2 | -3 | -5 | -3 | -2
1 | -2 | -3 | -2 | 1
1 | 1 | 1
0 | 0 | 0
-1 | -1 | -1
1 | 0
0 | -1
Good Localization
Noise Sensitive
Poor Detection
Poor Localization
Less Noise Sensitive
Good Detection

## Slide 56: Sobel Filter Problems
Poor Localization (Trigger response in multiple adjacent pixels)
Thresholding value favors certain directions over others
  Can miss oblique edges more than horizontal or vertical edges
  False negatives
Computer Vision

## Slide 57: Marr-Hildreth Edge Detector
Computer Vision

## Slide 58: David Marr – Ellen Hildreth
Computer Vision

## Slide 59: Second Derivative
Laplacian Filter
Maxima-minima of first derivative
Zero-crossings of second derivative
Computer Vision
Image
Profile of a horizontal line
(cross-section)
First derivative
Second derivative

## Slide 60: Marr-Hildreth Edge Detector [1980]
Computer Vision
Smooth image by Gaussian filter 
Apply Laplacian to
Find zero crossings
  Scan along each row, record an edge point at the location of zero crossing.
Apply threshold and mark edges
Repeat above step along each column

## Slide 61: Marr-Hildreth Edge Detector [1980]
Computer Vision
Gaussian
Laplacian of Gaussian

## Slide 62: Marr-Hildreth Edge Detector [1980]
Computer Vision
Laplacian of Gaussian
0 | 1 | 1 | 2 | 2 | 2 | 1 | 1 | 0
1 | 2 | 4 | 5 | 5 | 5 | 4 | 2 | 1
1 | 4 | 5 | 3 | 0 | 3 | 5 | 4 | 1
2 | 5 | 3 | -12 | -24 | -12 | 3 | 5 | 2
2 | 5 | 0 | -24 | -40 | -24 | 0 | 5 | 2
2 | 5 | 3 | -12 | -24 | -12 | 3 | 5 | 2
1 | 4 | 5 | 3 | 0 | 3 | 5 | 4 | 1
1 | 2 | 4 | 5 | 5 | 5 | 4 | 2 | 1
0 | 1 | 1 | 2 | 2 | 2 | 1 | 1 | 0

## Slide 63: Marr-Hildreth Edge Detector [1980]
Computer Vision
Zero crossings of

## Slide 64: Marr-Hildreth Edge Detector [1980]
Computer Vision

## Slide 65: Marr-Hildreth Edge Detector [1980]
Computer Vision

## Slide 66: Canny Edge Detector
Computer Vision

## Slide 67: Canny Edge Detector [1986]
Computer Vision
Smooth image by Gaussian filter 
Compute derivative of filtered image
Find magnitude and orientation of gradient
Apply non-max suppression
Apply thresholding (hysteresis)
John F. Canny

## Slide 68: Canny Edge Detector [1986]
Computer Vision
Gaussian
Derivative of Gaussian

## Slide 69: Canny Edge Detector [1986]
Computer Vision
Gaussian
x-direction
y-direction

## Slide 70: Canny Gradients
Computer Vision
Original
X-derivative of gaussian
Y-derivative of gaussian
Gradient Magnitude

## Slide 71: Gradient Orientation
Computer Vision
Original

## Slide 72: Non-Max Suppression
Computer Vision

## Slide 73: Non-Max Suppression
Computer Vision

## Slide 74: Non-Max Suppression
Computer Vision

## Slide 75: Non-Max Suppression
Computer Vision
Before Non-max Suppression
After Non-max Suppression

## Slide 76: Double Thresholds and Hysteresis
Identifying 3 kinds of pixels:
  Strong pixels (or High intensity)
    Surely contribute to the final edge
  Weak pixels
    “Not sure” area. Pixels with intensity not high, but not that low to be considered as non-relevant
  Non-relevant pixels (or Low intensity)
    Non edge
Computer Vision

## Slide 77: Double Thresholds and Hysteresis
Computer Vision

## Slide 78: Hysteresis
Wikipedia: The dependence of the state of a system on its history.
Our case: The dependency of a pixel on its neighbors.
  a Weak pixel will be categorized as High if it has at least High neighbor among its 8 neighbors.
Computer Vision

## Slide 79: Hysteresis
Computer Vision
Before Hysteresis Thresholding
After Hysteresis Thresholding

## Slide 80: Final Canny Edges
Computer Vision

## Slide 81: Effect of Gaussian Kernel
Computer Vision
Original
Canny with
Canny with
Notes: The choice of depends on desired behavior
•large detects large scale edges
•small detects fine features
The choice of 𝜎 depends on desired behavior
•large 𝜎 detects large scale edges
•small 𝜎 detects fine features

## Slide 82: Effect of Gaussian Kernel
Computer Vision
Original
Canny with
Canny with
Notes: The choice of depends on desired behavior
•large detects large scale edges
•small detects fine features
The choice of 𝜎 depends on desired behavior
•large 𝜎 detects large scale edges
•small 𝜎 detects fine features

## Slide 83
Computer Vision

## Slide 84: 45 Years History of Edge Detection
Computer Vision
[Pre-Deep Learning]

## Slide 85: 45 Years History of Edge Detection
Computer Vision
[With Deep Learning]
Notes: Liu-Richer

## Slide 86: Question?
Computer Vision

## Slide 87: Next Agenda
Descriptor
Feature Detection
Computer Vision

## Slide 88: References
Yogesh Singh Rawat – CAP5415 Lectures, University of Central Florida
David Fouhey – EECS442 Lectures, University of Michigan
Grauman, K. and Leibe, B. 2011. Visual Object Recognition. Synthesis Lectures Artif. Intell. Mach. Learn. 5, 1 181
Computer Vision